## Slide 1: Distributed Vision-Based Target Tracking Control Using Multiple Mobile Robots
Department of Electrical and Computer Engineering
Bradley University
5/1/2017
Anthony Le and Ryan Clue
Advisors: Drs. Jing Wang and In Soo Ahn
Notes: Add Page number
Add date

## Slide 2: Outline
Introduction
Overview of QBot2
Control Design
  Target Identification
  Control
  Integration
Experimental Results
Conclusions

## Slide 3
Introduction

## Slide 4: Introduction
Coordination control of multiple robots
Military and civilian applications
Environmental monitoring, threat/obstacle avoidance, search & rescue
Notes: Bullet points, images

## Slide 5: Motivation
In the study of distributed control, one of the fundamental problems is how to make a group of robots maintain certain geometric formation pattern while tracking a target.
Local sensing information exchange among robots is the key in the design of distributed control.
Notes: Short bullets, text too small
Only need keywords or short phrases

## Slide 6: Motivation
Vision sensors have been used in the localization, navigation, and control of the individual robot.
The use of vision sensors for distributed control of multiple robots should be studied.
Notes: Short bullets, text too small
Only need keywords or short phrases

## Slide 7: Related Work
Peter Corke, Robotics, Vision and Control and MATLAB vision control toolbox
2016 Senior Project: Cooperative Control of Heterogeneous Mobile Robots Network
Franchi, Stegagno, and Oriolo, Decentralized multi-robot encirclement of a 3D target with guaranteed collision avoidance. Feb 2016.
Notes: Not same as references, ALSO introduce work briefly

## Slide 8: Objective
Design a distributed vision-based target tracking control algorithm for multiple mobile robots
To achieve the above objective, the research tasks include:
  Target identification based on RGB image
  Target tracking algorithm based on robot model linearization
  Design leader-follower formation control algorithm
  Coordinate target identification module and target control module using Stateflow

## Slide 9
Overview of QBot2

## Slide 10: QBot2 Hardware

## Slide 11: QBot2 Hardware
Differential drive robot base has a maximum speed of 0.7m/s.
Color camera properties
  640x480 Resolution
  57°x43° Field-of-View
  Red, Green, Blue Color Channels with 8-bit Depth
Infrared Camera Properties
  640x480 Resolution
  52.5°x41° Field-of-View
  0.5m to 6m Depth Estimation (using IR emitter) with 11-bit Depth

## Slide 12: Robot Platform

## Slide 13: Kinect Camera

## Slide 14
 | RGB | Infrared
Field of View | 43° vertical x 57° horizontal | 41° vertical x 52.5° horizontal
Max. Frame Rate | 30 fps (or 9 fps) | 30 fps
Max. Image Resolution | 640x480 (or 1280x1024) | 640 x 480
Image Bit Depth | 8 bit color channels | 11 bits
Min/Max Functional Range | N/A | ~0.5m / ~5m
Camera Specifications

## Slide 15: QBot2 Software
The target computer is connected wirelessly with the host computer on which the SIMULINK model is running.
The control algorithms are developed in MATLAB/SIMULINK with QUARC on the host computer.
The control models are cross-compiled and downloaded to the target computer.

## Slide 16: Matlab Interface: Initialization Blocks
HIL Initialization
Targets a specific Hardware-in-the-Loop(HIL) board type
Allows cross-compilation of Matlab code for the deployment platform
Kinect Initialization
Required to use Kinect sensors
Outputs current state of the associated Kinect device

## Slide 17
Kinect Get Depth
Provides image of blobs with associated depth values
Utilizes Kinect’s capability to process IR image
Output values represent Cartesian distance in millimeters
Output type is 2D array of uint16
Kinect Get Image
Acquires either RGB or IR image
Stores image in Qbot2’s memory
Matlab Interface: Image Retrieval

## Slide 18
netsh wlan set profileparameter MY_SSID connectiontype=ibss connectionmode=manual
netsh wlan connect MY_SSID
Ad-hoc setting for windows 10
Set Fixed-step size (fundamental sample time) located in Quarc\Options\Solver
  This affects how frequently the Quarc interface samples the Matlab model for use by the DuoVero computer
  The computer can only reliably respond to the Quarc interface at 30Hz or less (default value is 1000Hz) due to image processing.
  In our project, the fundamental sample time is set to 0.1 seconds.
QUARC Environment Setup

## Slide 19
Control Design

## Slide 20: Target Identification
  RGB image and depth image are acquired via Get Image/Depth for target/robot identification.
  Image thresholding and blob detection algorithms are used in image processing.

## Slide 21: Blob Detection
Image Thresholding
  Isolate sections of an image by eliminating portions of the image whose values (RGB or IR) do not fall within a particular set of constraints
  Simplest method of image processing for RGB images
Blob Detection
  Accuracy entirely dependent on thresholding result

## Slide 22: Target Localization

## Slide 23: Target Localization

## Slide 24: Target Localization

## Slide 25: Alternative Design
Advantages of Color Thresholding
  Low processor resource requirements
Disadvantages of Color Thresholding
  White balancing
  Differences in lighting will drastically affect results
  Any source of outside light will require frequent threshold adjustments
Notes: Add one page before talking about the problems with color thresholding.
Also why these alternatives were not used

## Slide 26: Shape Detection

## Slide 27: Hough Transform

## Slide 28: Circle-Hough Transform

## Slide 29: Hough Transform

## Slide 30: Background Subtraction and Floor Determination

## Slide 31: Design of Control Modules
Depending on whether the robot is following a target or leader robots, two separate control modules are used
Both modules use X-Y values from the converted image of the image processing module.

## Slide 32: Robot Model
Kinematic Model
Using input-output linearization, linearized Model is obtained

## Slide 33: Target Encirclement Control
The linearized model is further transformed into cylindrical coordinates for encirclement control design.
Encirclement control laws are given by
where kr : proportional gain, : encirclement radius
: distance from robot to target

## Slide 34: Target Encirclement Control
The inverse of the Jacobian matrix is used to determine and
where
Notes: Robot model -> linearize -> convert linear to polar ->
Partial rho/px partial phi/px, rho/py phi/py (check this )

## Slide 35: Target Encirclement Control
and are then converted to Vc and
Vc and are converted to Vr and VL
Notes: Dimensions not right (fix the dimension here, should be col vector) be consistent in the equations (Vc )

## Slide 36: Encoder Transformation

## Slide 37: Leader-Follower Control
Leader-follower control module is used for distributed multi-robot coordination
Image processing is used to localize the leader robot coordinates () in the vision sensor range
The following leader-follower control laws are implemented
where Kv=0.2 and Kw= 0.5. Limits for angular and forward velocity are set to 0.2 m/s
Notes: Double check atan ( ), It is better to use tan^-1( yr/xr)

## Slide 38: Event-based System Control
• Stateflow control is designed to coordinate control modules enabling/disabling Simulink blocks Stages
  Step 1: Search for encirclement target or leader robot. If target is not in view, rotate 15° CCW and repeat this step. Otherwise continue to next stage.
  Step 2: Switch to encirclement or leader-follower motion controls. If target is no longer in view, stop moving and return to step 1.
Notes: Add a flow chart

## Slide 39
Event-based System Control: Stateflow

## Slide 40
Event-based System Control – Encirclement Control

## Slide 41
Leader-Follower Control
Event-based System Control
Notes: Fix the title, - Leader-follower control ( 40 font size)

## Slide 42: Event-based System Control
Encirclement Control
Leader-Follower Control

## Slide 43: Event-based System Control
Notes: Add subtitle with font size 40 here
Add arrow and box to highlight the control blocks

## Slide 44: Event-based System Control
Notes: Add subtitle with font size 40 here
Add arrow and box to highlight the control blocks

## Slide 45: Event-based System Control
Notes: Add subtitle with font size 40 here
Add arrow and box to highlight the control blocks

## Slide 46: Event-based System Control
Notes: Add subtitle with font size 40 here
Add arrow and box to highlight the control blocks

## Slide 47
Experimental Results

## Slide 48: Experimental Results - Encirclement
Notes: Add video

## Slide 49: Experimental Results - Encirclement
Phase plot of robot
Forward and Angular Velocities
Notes: TITLES!
Must add some labels, legends
Add a little bit of context

## Slide 50: Experimental Results – Encirclement

## Slide 51: Experimental Results – Leader-Follower

## Slide 52: Experimental Results – Leader-Follower

## Slide 53: Experimental Results – Leader-Follower
Phase plot of robot
Forward and angular velocities of robot
Notes: Mark the start in the phase plot

## Slide 54: Division of Work
Ryan
  Image Processing Module Design
  Encirclement Stateflow Control Design
  Experimental Testing
Anthony
  Image Processing
  Control Module Design
  Leader-Follower Stateflow Control Design
  Experimental Testing
Notes: Your full name

## Slide 55: Conclusions
  Work accomplished
    A distributed vision-based target tracking control was designed and experimentally validated using mobile robots.
    The design was done by combining image processing and control task modules using Stateflow switched control strategies.
  Future work
    Develop a more effective and robust image processing method
      Shape Recognition
    Integrate obstacle avoidance function
    Conduct experiments using a large group of robots
Notes:     Use encirclement control instead of leader-follower control
      Where robots assume other robot’s movement

## Slide 56
Notes:     ACK.

## Slide 57: References
[1] “Cooperative Control of Heterogenous Mobile Robots Network.” [Online]. Available: http://ee.bradley.edu/projects/proj2016/mrn/. [Accessed: 14-Dec-2016].
[2] A. Franchi, P. Stegagno, and G. Oriolo, “Decentralized Multi-Robot Encirclement of a 3D Target with Guaranteed Collision Avoidance,” Autonomous Robots, vol. 40, no. 2, pp. 245–265, Feb. 2016.
[3] G. Bock, R. Hendrickson, J. Lamkin, B. Dhall, J. Wang, and I. S. Ahn, “Experiments of distributed control for multiple mobile robots with limited sensing/communication capacity,” in 2016 IEEE International Conference on Electro Information Technology (EIT), 2016, pp. 0559–0564.
[4] “Kinect for Windows Sensor Components and Specifications.” [Online]. Available: https://msdn.microsoft.com/en-us/library/jj131033.aspx. [Accessed: 14-Dec-2016].
[5] “Quanser - QBot 2 for QUARC.” [Online]. Available: http://www.quanser.com/products/qbot2. [Accessed: 14-Dec-2016].
[6] P. Corke, Robotics, Vision and Control - Fundamental Algorithms in MATLAB .
Notes: Follow structure for citations like in report
Also peter corke’s book and toolbox

## Slide 58: Q&A
Thanks!